## Slide 1
STATISTICAL ANALYSES TO IMPROVE GAS TURBINE DIAGNOSTICS RELIABILITY
R. Bettocchi, M. Pinelli, P. R. Spina, M. Venturini
Dipartimento di Ingegneria – University of Ferrara
      Ferrara – ITALY
Notes: Thank you Mr. Chairman,
just few words to introduce the research team which I belong to, which is the Energy Systems research team of the University of Ferrara (Italy).
Since several years my research team has been involved in developing techniques for the diagnosis of gas turbine health state determination and computational programs for the assessment of gas turbine operating state, by using both “traditional” approaches (GPA) and by using Artificial Intelligence techniques (Expert Systems, Neural Nets and Fuzzy Logic).
Another field of activity is that of measurement reliability. Several techniques, based on Gas Path Analysis, identification models and on statistics, were set up and applied.
Our experimental activity deals with the study of small size compressors for gas turbines in order to establish correlations between induced faults (fouling, erosion, tip clang) or anomalous operating conditions (water or dust ingestion) with measurement variations. The response is evaluated both from stationary performance evaluation and by means of dynamical responses.
In this contest, I present a paper which deals with the “Improvement of the reliability in Gas Turbine Health State Determination by using statistical analyses on gas turbine failures”.

## Slide 2: Introduction (1/2)
Optimization of gas turbine O & M
Increase in machine availability
Reduction of management costs
ON-CONDITION maintenance
SCHEDULED maintenance
supported by
Notes: The optimization of industrial gas turbine operation and maintenance, together with the increase in machine availability and the reduction of management costs, can be achieved through the knowledge of the gas turbine actual operating state.
In fact, the predominant strategy for industrial gas turbine maintenance is the scheduled maintenance, which is performed according to a priori schedules, regardless of the effective gas turbine health state. This strategy may cause relevant costs related to gas turbine non-scheduled stops, which mean the reduction or the interruption of the process and consequent repairing actions.
An increase in machine availability and a reduction of costs can be achieved if the regular maintenance is supported by the on condition maintenance. The on condition maintenance is based on ad hoc actions, derived from the knowledge of the machine actual operating state.

## Slide 3: Introduction (2/2)
ON-CONDITION maintenance
Actual gas turbine Health State knowledge
Information from the diagnostic process
(1) how far the actual machine operating condition is from the expected one
(2) which components are degraded
(3) the causes of malfunctioning
ALLOWS
(a) in-advance planning of maintenance stops
(b) performing on-line maintenance actions
(c) adapting GT control logic
requires
Notes: The on condition maintenance is based on ad hoc actions, as we have said before, which can be derived from the knowledge of the machine actual operating state.
One of the most widespread techniques for gas turbine health state determination is the Gas Path Analysis (GPA), which will be briefly described in the following. The information which can be obtained from the GPA diagnostic process are summarized below. It is possible to establish
(i) how far the actual machine operating condition is from the expected one
(ii) which components are degraded
(iii) the causes of malfunctioning.
Thus, the up-to-date knowledge of the gas turbine health state allows
(i) in-advance planning of maintenance stops, depending on the actual gas turbine health state, on the availability of stand-by machines and on the production requirements;
(ii) performing on-line maintenance actions;
(iii) adapting the gas turbine control logic to the machine actual health state and, in the worst cases, to stop the machine to prevent from faults that may even compromise machine integrity.

## Slide 4: Objectives
Statistical analysis of occurrence and incidence of failures by using information from literature and databases of maintenance reports
Application of the methodology to a two shaft 10 MW gas turbine with variable power turbine nozzle
To improve the reliability of the diagnostic process when techniques for gas turbine Health State determination are used, the following items are developed:
Set-up of a methodology for the identification of the best combination of measurements and health indices that should be used for the determination of the gas turbine health indices with the minimum uncertainty (Weighted Reward Number)
Notes: One of the most critical problems that has to be faced when GPA techniques are applied is the reliability of the information that can be obtained (which depends on several factors, as, for example, the capability of the Cycle Program to accurately reproduce the actual gas turbine thermodynamic cycle, the accuracy of field measurements, the limited availability of measured variables on the gas turbine and the fact that some of the characteristic parameters to be estimated have to be kept constant during the calculations).
So, in order to improve …

## Slide 5: Gas Turbine Fault Incidence
Sources of information
(1) manuals for turbomachinery maintenance (Sawyer and Hallberg, 1980)
(2) study on GT availability and performance (Singh R., 1999)
(3) database developed by gas turbine users (OREDA, 1999)
The analysis is oriented to establish, on a statistical basis, the incidence and the severity of machine malfunctions and failures
Information (1) was used by gas turbine manufacturers to schedule maintenance actions in order to prevent failures
Information (2) and (3) reports the malfunctions which took place regardless of the scheduled maintenance. In fact, the scheduled maintenance plan is intended to minimize the failure typologies as in (1)
Notes: In order to define a scheduled maintenance program, it is fundamental to know the component life and the rate of performance decrease as a function of running hours and type of installation. This can be done by analyzing gas turbine historical data over a long period. The analysis is oriented to establish, on a statistical basis, the incidence and the severity of machine malfunctions and failures, in relation to typology (heavy-duty, aeroderivative, single or two shaft, etc.), installation site (land, off-shore) and operating regime (base load, alternate, stand-by).
The knowledge of failure incidence can be useful also for the development and application of on condition maintenance. In fact, as explained in the following paragraph, the use of indices related to the probability that a given failure may occur allows the uncertainty in gas turbine health state determination to be reduced.
Different sources of information about failure occurrence and typology are available …
It should be reminded that information as in (1) reports the malfunctions which took place regardless of the scheduled maintenance and so the percentage incidence is completely different from (2) and (3). In fact, the scheduled maintenance plan is intended to minimize the failure typologies as in (1).

## Slide 6
Results of an insurance company over a 10-year period Sawyer and Hallberg (1980)
Study on GT availability and performance presented at 44th GT Users Association Conference (Singh R., 1999)
Notes: The Table below (Sawyer and Hallberg, 1980) reports the results of the experience of one insurance company over a 10-year period with failures or incidents involving gas turbines. Blade failures (compressor and turbine) comprise the largest group of failures (35%). Next in the order are fires and explosions in the combustor and turbine sections. Information of the type reported in Table 1 is used by gas turbine manufacturers to schedule maintenance actions in order to prevent failures. This is usually done by substituting the most critical component at scheduled times.
A statistical analysis of GT failures was presented by Prof. Singh . In this case, owing to the scheduled maintenance, compressor and turbine faults are negligible, while the highest percentage incidence is that of GT control system.

## Slide 7
Database developed by gas turbine users (OREDA, 1999)
219
(3.196.085 h)
Gas turbines
heavy-duty
145
aeroderivative
74
Tipology
Regime
Base load
Alternate
Stand-by
Notes: As done by Prof. Singh, we also developed a statistical analysis on the data derived from OREDA database.
The OREDA (Offshore REliability DAta) consortium groups a great number of companies involved in oil and gas treatment, which are also gas turbine users. In particular, the 1999 OREDA handbook edition reports data referring to 219 gas turbines working in off-shore sites for a total amount of 3.196.085 firing hours.
In the figure, the results in terms of percentage incidence of the failures, affecting the main components of a gas turbine are reported. This was done both for all the available machines and by dividing them into two main classes: aeroderivative and heavy-duty: It can be observed that the most critical components are the monitoring and control system and the gas generator. Moreover, it can be noticed that failure incidence depends slightly from machine typology (aeroderivative or heavy-duty).
Tables 2 shows in detail, for all the 219 considered gas turbines, the failure percentage incidence for the gas generator and power turbine sub-components.

## Slide 8
Further RESULTS (OREDA, 1999)
heavy-duty gas turbines (base load): smallest number of FpM
the most critical gas turbines are the aeroderivative machines with alternate operating regime
MTBF values are in quite good agreement with FpM
stand-by machines: relatively low MTBF values since a quite high number of faults corresponds to a low number of working hours
Notes: Further results from the analysis of OREDA database are reported in the two Figures.
From the Figure on the top, it can be observed that heavy-duty gas turbines, working at base load, have the smallest number of faults per machine, while the most critical gas turbines are the aeroderivative machines with alternate operating regime.
From the Figure on the bottom, it can be observed that MTBF values in this Figure are in quite good agreement with faults per gas turbine in the Figure on the top, i. e. highest reliability for heavy-duty gas turbine working at base load and high criticality for aeroderivative machines with an alternate operating regime. As regards stand-by machines, they present relatively low MTBF values since a quite high number of faults (see Figure above) corresponds to a low number of working hours.

## Slide 9
Qm, QWP : measurable parameters
Xf : fixed characteristic parameters
Xv : variable characteristic parameters
Field measurements
Health indices
Assessment of gas turbine health state through GPA techniques
X
vn
v1
 efficiency
 mass flow function
p pressure drop
wp1
wpt
Q
Q
X
Q
m1
Q
mn
X
f
1
X
fk
GPA model
GPA: GT health indices can be determined by solving in inverse mode the mathematical model of the gas turbine thermodynamic cycle
Notes: The Gas Path Analysis based model evaluates the gas turbine health indices X by solving in inverse mode the program for the thermodynamic cycle calculation.
The inputs of the program are:
- the measurements that unequivocally determine GT working point (QWP);
- the measurements taken along the gas path (Qm);
- the indices that have to be fixed (i.e. considered constant) since the number of variable parameters Xv depends on the number of available measurements.
The calculation is performed by "adapting" the indices (“varying”), until the computed estimates of the measurable parameters agree with the values measured on the gas turbine. The health indices are efficiencies, characteristic flow passage areas and pressure drops for each component.
The comparison between the actual values and the ones in the "new and clean" condition allows the evaluation of the shifts between the actual gas turbine operating state and the expected one, and the localization of inefficient operations due to deterioration and faults. Since actual gas turbine Health State determination is performed by means of health indices, it is advisable to determine them with the lowest uncertainty.

## Slide 10
The number and type
of health indices to be investigated
have to be chosen according to
- available measurements (number and type)
(the system equation Xv=F(Qm, QWP, Xf) has to be determined)
- health indices that usually vary
(representative of the most critical components)
- minimization of uncertainties affecting the calculation of health indices, taking into account that Engine Health State determination has to be more accurate for the components that are most subjected to faults
1
2
Notes: In fact, the number and type of … leggere tutto

## Slide 11
Xv = F (Qm, QWP, Xf) = F (Y)
The solution Xv is affected by variations of
- Qm and QWP (due, for example, to measurement errors)
- Xf (the parameters kept constant in the calculation may vary in the actual machine, for instance due to the aging and deterioration)
Relative error on each variable parameter Xvj of the vector Xv
Sources of errors in parameter estimation
n: # of Qm measured variables
t: # of working point measured variables QWP
s: # of the parameters kept constant Xf
ij = (Yi/Xvj) (∂Xvj/∂Yi) : sensitivity coeff.
Notes: As can be seen, the solution Xv of the Equation is affected by variations of Qm and QWP (due, for example, to measurement errors) and of Xf. In fact, the parameters kept constant in the calculation, may vary in the actual machine, for instance due to the aging and deterioration of gas turbine components.
The relative error on each variable parameter Xvj of the vector Xv due to these variations can be expressed as shown below, where n is the number of the gas path measured variables and of the variable parameters, t the number of working point measured variables, s the number of the parameters kept constant and ij are the sensitivity coefficients defined as ij = (Yi/Xvj)(DXvj/DYi)

## Slide 12
Choice of the best combination of measurements and parameters through a Reward Number
If ΔYi/Yi are all assumed equal to 1, RN is independent of ΔYi amount and only depends on the considered combination of measurements and parameters
Greatest value of RN => the average-root-sum-square of the relative errors Xvj/Xvj on all the variable parameters is minimum.
Notes: In order to compare different measurement/parameter combinations, the authors have introduced a “Reward Number” (RN) defined as the inverse of the average-root-sum-square of the errors on all the considered variable parameters. In the calculation of RN all the relative variations Yi/Yi were expressed in percentage and assumed equal to 1, so that RN is independent of Yi amounts, and is only dependent on the considered measurement/parameter combination. Therefore, RN assumes the expression reported here.
The measurement/parameter combination characterized by the greatest value of RN is the one for which the average-root-sum-square of the errors on all the variable parameters is minimum.

## Slide 13
Weighted Reward Number
THE PROBLEM: since each GT failure presents a different probability of occurrence, the characteristic parameters associated to the most probable failures should be calculated with the highest accuracy.
The combination factor fc takes into account the presence (j = 1) or the absence (j = 0) of each Xj-th parameter (j= 1,…, n+s) in a given variable parameter set Xv.
weights depend on the probability that a fault can occur
wj   criticality of the component   reconstruction accuracy
Notes: However, not all the parameters indices of the gas turbine health state have the same importance for the operating state assessment of gas turbines. In fact, as shown in the previous section, each failure presents a different probability of occurrence, and, so, the characteristic parameters associated to the most probable failures should be calculated with the highest accuracy.
To take into account this fact, a “Weighted Reward Number” (RNw) has been introduced defined as reported in the relation. In the expression of RNw:
1. the weights wj depend on the failure probability; the higher is the weight, the higher is the criticality of the corresponding characteristic parameter and, so, the higher is the desired calculation accuracy;
2. the combination factor fc is used to take into account the presence (j equal to 1) or the absence (j equal to 0) of each Xj-th parameter (j= 1,…, n+s) in a given variable parameter set Xv.
NOTA_1 I componenti critici, cioè quelli che hanno maggiori probabilità di guasto, devono avere bassa  perché li devo calcolare con elevata accuratezza. Quindi, se metto un peso alto w, lo faccio per sentire l’influenza di . Se lo mettessi a zero, non lo sentirei nemmeno se fosse alto.
NOTA_2 Il valore di RNw ha solo un significato comparativo, non assoluto. Il suo valore varia da 0 a infinito (caso in cui l’errore di ricostruzione è zero).

## Slide 14
Methodology for weights selection
1. Statistical analysis of failure occurrence
2. Assignment of GPA health indices Xj to each gas turbine failure type
a) Some failure may not affect any parameter (e.g. fuel control system failure)
b) Some failure may affect more than one parameter
4. Calculation of the relative incidence for each health index (the sum makes 1)
3. Calculation of total failure incidence for each GPA health index
e.g.: Compressor mass flow function C is influenced by compressor stator and rotor failures: 0.2 + 0.3 = 0.5 %
Notes: The choice of the weights is performed according to the probability that a failure may occur. The methodology for weight selection consists of four steps:
1. Statistical …
2. Assignment of GPA characteristic parameters Xj to each gas turbine failure type, as shown in Table 4. Since Gas Path Analysis techniques can only detect the gas-path failures that have observable effects on the measurable variables (Ogaji et al., 2002), some of the failures reported in Tables 1, 2 and 3, may not be detected, i.e. they are not assigned to any characteristic parameter. On the contrary, since some failures may affect more than one parameter, the corresponding incidence was assigned to each parameter. The only exceptions were the case of "Blade tip rubs" reported in Table 1, for which the incidence was equally divided between compressor and gas generator mass flow functions, and the case of "Turbine" reported in Table 3, for which the incidence was equally split between the gas generator and the power turbine.
3. Calculation of total failure incidence related to each GPA characteristic parameter;
4. Calculation of the relative incidence for each characteristic parameter, by normalizing failure incidence values so that the sum makes one.

## Slide 15
Application of weights selection methodology
Sawyer and Hallberg (1980): the sum in column 1 is greater than 100 % (some failures were assigned to more than one parameter)
the results derived from OREDA (1999) and (Singh R., 1999) are in good agreement
Notes: The Table shows the numerical results for the three analyzed situations. In Sawyer and Hallberg (1980), the sum in the first column is greater than 100% since some failures are assigned to more than one parameter.
Failure incidences reported in the third and in the fifth column of Table 5 are derived from Table 2 and 3, respectively. It is interesting to notice that the results derived from OREDA (1999) and Ogaji et al. (2002) are in good agreement each other

## Slide 16
RNw1 - RNw7: sensitivity analysis on any single parameter
RNw8 - RNw10: sensitivity analysis on main components
RNw11: Sawyer and Hallberg (1980)
RNw12: OREDA (1999)
RNw13: Singh R. (1999)
Weights combinations
Notes: Now, let’s see the weights combinations that were chosen for the analysis performed in the paper..
The Table shows the considered values for the weights used to calculate RNw. First, a sensitivity analysis with respect to any single parameter was performed (RNw1 through RNw7). Then, the sensitivity analysis was extended to the main components: through RNw8, RNw9 and RNw10, the critical component is considered to be the compressor, the gas generator turbine and the power turbine respectively. Finally, the weights used in RNw11, RNw12 and RNw13 were chosen in accordance with failure occurrence estimated through the statistical analysis that was carried out above (Table 5). In particular, the weights used for RNw11 calculation were derived from Sawyer and Hallberg (1980), the RNw12 was referred to OREDA (1999) data and the RNw13 was obtained from Ogaji et al. (2002).
If the manufacturer or the user has at disposal other data, the values of weights can be updated.

## Slide 17
Analyzed cases (2-shaft with variable NGV 10 MW gas turbine)
Notes: The RNw calculations performed consider seventeen possible measurements/health indices combinations were chosen among the most significant cases that can be encountered in practice (Pinelli and Spina, 2000b). These combinations are reported in details in the Table.
For instance, in case 15, the available measurements are pressure and temperature at the compressor outlet, exhaust gas temperature, variable nozzle angular position, pressure between the two turbines (at the gas generator turbine outlet) and air inlet mass flow rate.
The calculated health indices are the efficiency and the mass flow function for the Compressor, for the Gas Generator turbine and for the Power turbine.
Among the analyzed cases, it was considered that 3 measurements are always the same (poc, Toc e Tot) and then some other measurements are added.

## Slide 18
7 Qm: for the analysis of all single parameters and components, MiC better than ToGGT
6 Qm: intermediate pressure poggt instead of mass flow rate measurement (Case 15) is advisable, though combustor efficiency can not be determined
4 Qm: no information can be obtained about power turbine and combustor
Results of the sensitivity analysis
6 available measurable quantities
Notes: The best measurement/parameter set should be identified for any given number and kind of available measured variable set: this is the situation that can be encountered in practice when a given instrumentation set is present on the machine and the most appropriate parameter combination has to be chosen. Furthermore, the analysis that was carried out should lead to the identification of the most significant measurements which would be useful to be performed in addition to the ones that are already available.
The results of the sensitivity analysis are reported on a component-basis.
In the two extreme situations (4 or 7 available measurements), the results can be summarized as:
1. with four available measured variables no information can be obtained about power turbine and combustor;
2. if seven measurements are available, Case 17 is recommended for the analysis of all single parameters and components.
In the intermediate case of six available measurements (which is a typical case for the considered gas turbine), the results are reported in details. Form the Figure, it can be noticed that when six measured variables are available, the absence of Mf measurement (Case 15) is advisable for compressor, gas generator and power turbine analysis, though combustor efficiency cc can not be determined.

## Slide 19
7 Qm (case 16-17): better to add Mic instead of Toggt (case 17)
6 Qm (case 7-15): case 15 (poggt and Mic available) is the best
4 Qm (case 1-2): better to use VN rather than Mf (case 2)
Application of the Weighted Reward Number
5 Qm (case 3-6): case 3 is the best
Notes: According to failure occurrence derived from the three sources of information, three Weighted Reward Numbers (RNw11, RNw12 and RNw13) for the three weight combinations 11, 12 and 13 were calculated. For all measurement/parameter combinations (Cases 1 through 17), the results are reported in the Figure. It can be noticed that:
1. if four measured variables are available (Cases 1 and 2), Case 2 (poc, Toc, Tot and VN instead of Mf) is the best independently of the considered weight combination, in agreement with a previous analysis conducted by Pinelli and Venturini (2001);
2. if five measured variables are available (Case 3 to 6), Case 3 is the best, for all the three considered weight combinations;
3. if six measured variables are available (Cases 7 to 15), the best Case is 15 for all the three considered weight combinations;
4. if seven measured variables are available, Case 17 is better than Case 16. So, it seems better to have the inlet mass flow rate measurement (Case 17) instead of Toggt measurement (Case 16) for all the three considered weight combinations. Anyway, it should be paid attention to the fact that Mic measurement accuracy may be lower than the one for Toggt.

## Slide 20
Conclusions
Methodology to improve the reliability in
gas turbine health state determination
identification of the most appropriate parameter combination with respect to a given instrumentation set
choice of the most significant measurements to perform in addition to the ones which are already available on the gas turbine
The methodology has a general validity, but the results depend on gas turbine configuration (i.e. # of measurable variables)
Notes: In this paper, a methodology to improve the reliability in gas turbine health state determination has been developed, by optimizing the choice of the best measurement/parameter combination in accordance with the incidence of failures that affect the gas turbine under investigation.
The analysis of failure incidence, performed through data which were collected from bibliography and from ad hoc databases, allowed the determination of factors to weigh the different possible measurement/parameter combinations.
For any given number and kind of available measured variables, the best measurement/parameter set was identified. This allows (i) the identification of the most appropriate parameter combination with respect to a given instrumentation set and (ii) the choice of the most significant measurements to perform in addition to the ones which are already available on the gas turbine.
The methodology has a general validity, though the results depend on gas turbine configuration (i.e. # of measurable variables).