## Slide 1: Gas Turbine (ABB GT10)
Notes: The above methodology found its way of application on a twin shaft gas turbine (ABB GT10), installed at Rhodes island, and owned by Public Power Corporation (PPC) of Greece.
The chronicle of the application may be summarised as follows.
During a first phase, the problem was to identify the cause of the observed EGT increase.
Once the problem was identified, corrective action was taken and it was necessary to verify the effectiveness of the interventions done on the engine.
The analysis performed in each case is described in the following.
Data collected from the initial operation of the engine as well as those from efficiency testing were analysed for performing a diagnosis. The analysis of the data was made at two levels:
- First, a "common sense" thermodynamic analysis was performed, by executing mainly heat balance calculations.
Such calculations can provide non-measured quantities from the values of measured ones, and give a comparative picture of parameters characterising engine condition.
The guidelines of ISO 2314 correction and calculation procedures were applied for this purpose.
Measured and calculated values of various thermodynamic quantities are reduced to operation with standard day ambient conditions.
- Second, a more elaborate procedure, namely the adaptive performance modelling mentioned above, has been applied.

## Slide 2
Gas Generator Turbine 1st rotor blades.
Notes: Indeed the inspection confirmed the initial diagnosis for the condition of the turbines. Deposits were found in both gas generator and power turbine blades.
The deposits were due to anticorrosive additives of the fuel.
Figures 5 to 8 illustrate the condition of the blades. Figures 5 and 6 show the first rotor and stator of the compressor turbine, respectively.
The deposits have the form of a uniform coat, which has partially cracked on the rotor blades.
Part of the deposit layer has been removed in the picture of the vanes, Fig. 6, to indicate the make more apparent the presence of the layer.

## Slide 3
Power Turbine 2nd Stator vanes detail.
Power Turbine 2nd Stator vanes. Leading edge pressure side view.
Notes: While stator vanes of the power turbine are also covered by a more or less uniform coat of deposits, Figure 7, deposits on the rotor blades give a rougher surface, Figure 8.
Although the photos are taken using an ordinary camera, the layer of deposits is well discriminated.
A corrective action was necessary.
Two alternative approaches were considered.
The first one consisted in cleaning the blades while the later to perform geometry modification.
The manufacturer considers deposition as an unavoidable process, when oil is used as a fuel.
Fuel oil treatment with additives is essential in order to increase ash melting point and thus minimise the risk of blade corrosion (Olsson et al 1968).
He also alleges that this process is taking place during a small period during the beginning of the operation of the engine, when this layer is formed and thereafter no considerable changes are taking place.
Therefore, performance recovery was suggested to be based on component re-matching, resulting from the modification of the stagger angle of power turbine stator vanes.
Such possibility was foreseen on this engine, in order to remedy situations as the present one