## Slide 1
R. Bettocchi 1, P. R. Spina 2
1 Dipartimento di Ingegneria - University of Ferrara 2 DIEM - University of Bologna
Italy
A METHOD FOR THE DIAGNOSIS OF
GAS TURBINE SENSOR FAULTS
IN PRESENCE OF MEASUREMENT NOISE

## Slide 2
INTRODUCTION
The updated knowledge of the gas turbine operating state and the determination of the causes of performance degradation allow to maximize the availability of a gas turbine plant
The determination of the machine operating state requires the use of reliable measurements

## Slide 3
INTRODUCTION cont.
Measurement reliability may be increased by adopting sensor fault diagnostic techniques
The diagnostic technique effectiveness depends on the capability in:
- the detection of faults in presence of model inaccuracy and measurement disturbances, avoiding false alarms
- the unambiguous isolation of faults

## Slide 4
INTRODUCTION cont.
In the case of parity equation-based diagnostic techniques the use of a model incidence matrix with a column-canonical structure (i.e., each matrix column with the same number of zeroes, but in different positions) allows the obtainment of a robust method for the high-threshold isolation of single faults

## Slide 5
SENSOR FAULT DIAGNOSIS METHOD
Model-based diagnostic techniques: the fault detection and isolation is performed by analyzing the residuals obtained from the comparison between measured and computed values of the same quantities
Identification of a number of ARX (Auto Regressive eXogenous) MISO (Multi-Input/Single-Output) models equal to the number of gas turbine measurable outputs
(each model estimates the value of a measurable output starting from other input-output measured on the gas turbine)

## Slide 6
SENSOR FAULT ... cont.
Parity equations to evaluate the residuals

## Slide 7
"Fault" (or "incidence") matrix: matrix obtained from the model coefficient matrix "F" by substituting the coefficients with values "0" or "1" on the basis of whether they are zero or not
Each fault matrix column represents the fault signature of the corresponding sensor
Condition for the zero-threshold fault isolation (case of single faults): fault matrix columns linearly independent
SENSOR FAULT ... cont.

## Slide 8
SENSOR FAULT ... cont.
Fault isolation in presence of model inaccuracy and measurement noise
The presence of model inaccuracy and measurement noise requires thresholds on the residuals to minimize false alarms
When a fault occurs, the fault signature is obtained by substituting the residuals with values "0" or "1" on the basis of whether they are lower or higher than thresholds

## Slide 9
SENSOR FAULT ... cont.
For small amount faults, one or more residuals may remain under the threshold (fault signature degradation)
If the degraded fault signature is equal to another fault signature (i.e., to one of the fault matrix columns), an incorrect fault alarm occurs
Condition for the unambiguous isolation of single faults (high-threshold fault isolation): no fault matrix column can be obtained from another one by means of a degradation

## Slide 10
SENSOR FAULT ... cont.
Sufficient condition for the high-threshold fault isolation: incidence matrix with a column-canonical structure (i.e., each matrix column has the same number of zeroes, but in different positions)
This matrix structure allows the determination of a fault signature degradation avoiding an incorrect fault alarm (i.e., a fault signature with a number of zeroes higher than the one common to all the fault matrix columns, highlights a fault signature degradation)

## Slide 11
SENSOR FAULT ... cont.
A small amount fault is always detected, whereas the fault isolation is possible only when the fault amount is higher than the one generating the fault signature degradation
An analysis was performed on the minimal faults which can be isolated

## Slide 12
SENSOR FAULT ... cont.
A fault matrix with column-canonical structure was built starting from models of the gas turbine having the inputs ordered based on their influence on the model output accuracy and eliminating the inputs starting from the less influential ones

## Slide 13
SENSOR FAULT ... cont.
Input ordering process (for each model):
    1) identification of the SISO models, each of which having one of the gas turbine input-output measurable quantities as input;
    2) selection of the SISO model having the best accuracy;
    3) identification of the two-input MISO models, obtained by starting from the best SISO model and adding, in turn, one of the remaining gas turbine input-output measurable quantities which have not been used as input;
    4) selection of the two-input MISO model having the best accuracy;
    5) repetition of steps (3) and (4) as many times as is the number of all the gas turbine input-output measurable quantities, until MISO models are obtained having a number of inputs equal to the number of all the gas turbine input-output measurable quantities.

## Slide 14
SENSOR FAULT ... cont.

## Slide 15
MINIMAL SENSOR FAULT TO BE ISOLATED
FOR A GAS TURBINE APPLICATION
(I1) VIGV angular position
(I2) fuel mass flow rate
(O1) pressure at the compressor inlet
(O2) pressure at the compressor outlet
(O3) pressure at the turbine outlet
(O4) temperature at the compressor outlet
(O5) temperature at the turbine outlet
(O6) electrical power
C
T
ED
CC
I D
EG
IGV
O6
O1
O4
O2
O5
O3
I 1
I 2
O7

## Slide 16
MINIMAL SENSOR FAULT ... cont.
A number of models equal to the number of gas turbine measured outputs was built, each model calculating the value of a measurable output starting from all the inputs and outputs measured on the machine
The models have the inputs ordered based on their influence on the model output accuracy
The models were identified using time series of data generated with a non-linear dynamic gas turbine model

## Slide 17
MINIMAL SENSOR FAULT ... cont.
Noise standard deviations (% of the reference value) and reference values

## Slide 18
MINIMAL SENSOR FAULT ... cont.
The fault matrix with column-canonical structure related to the 6 gas turbine models requires a minimum of 2 zeroes per column
The fault matrix with canonical structure was built by eliminating the model inputs starting from the less influential ones, but with the condition for obtaining 2 zeroes per column in different positions

## Slide 19
Incidence matrix with column-canonical structure
with 2 zeroes per column
Residual
res (pic)
res (poc)
res (pot)
res (Toc)
res (Tot)
res (Pe)
pic
poc
pot
Toc
Tot
Pe

Mf
1
1
1
0
1
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1
0
1
1
0
1
0
0
1
1
1
0
1
1
0
1
1
1
0
1
1
1
0
1
0
1
0
1
1
MINIMAL SENSOR FAULT ... cont.

## Slide 20
Step faults of different amounts were simulated to determine the minimal faults to be isolated
MINIMAL SENSOR FAULT ... cont.

## Slide 21
MINIMAL SENSOR FAULT ... cont.
It is necessary to adopt methods to reduce the minimal faults to be isolated

## Slide 22
REDUCTION OF THE MINIMAL SENSOR FAULT
TO BE ISOLATED
To reduce the minimal sensor faults which can be isolated two different actions can be taken:
1) reduction of fault detectability thresholds
2) increase of residual sensitivities with respect to faults

## Slide 23
REDUCTION OF ... cont.
1) The fault detectability thresholds were reduced by reducing the residuals in fault-free conditions due both to model approximation and noise
This was done by filtering:
a) the time series of data used in the model identification phase
b) the time series of data used for the simulations
c) the residuals obtained by the simulations
First order digital filter:

## Slide 24
REDUCTION OF ... cont.
Full filtering: case of filtering the time series of data used in the model identification phase, in the simulations and the residuals obtained by the simulations

## Slide 25
REDUCTION OF ... cont.
REDUCTION OF ... cont.
2) The increase of residual sensitivities with respect to faults was obtained by using gas turbine models characterized by a fault matrix with 3 zeroes per column
The elimination of the less influential model inputs to obtain a fault matrix with 3 zeroes per column leads to residuals having a higher sensitivity with respect to faults

## Slide 26
Incidence matrix with column-canonical structure
with 3 zeroes per column
Residual
res (pic)
res (poc)
res (pot)
res (Toc)
res (Tot)
res (Pe)
pic
poc
pot
Toc
Tot
Pe

Mf
1
1
0
0
1
0
0
1
1
1
0
0
0
1
1
0
0
1
1
1
0
1
0
0
1
0
0
0
1
1
0
1
0
0
1
1
1
0
1
0
1
0
0
0
1
0
1
1
REDUCTION OF ... cont.

## Slide 27
REDUCTION OF ... cont.
Full filtering: case of filtering the time series of data used in the model identification phase, in the simulations and the residuals obtained by the simulations

## Slide 28
CONCLUSIONS
The parity equation-based diagnostic technique, which uses a fault matrix with a column-canonical structure, allows the unambiguous isolation of single gas turbine sensor faults, in presence of model inaccuracy and measurement noise
Minimal faults to be isolated acceptable for industrial applications can be obtained only by using a fault matrix with more than two zeroes per column and by filtering the time series of data used in the model identification phase, in the simulations and the residuals obtained by the simulations

## Slide 29
The technique, even if, in the best case, allows the isolation of minimal faults which are from 3 to 6 times the standard deviation of the measurement noise, presents a good reliability towards false alarms due to fault signature degradation
Improvements may be obtained by increasing the number of zeroes per column of the fault matrix and by using statistical tests on the residual whiteness, instead of comparing the residual amounts with fixed thresholds (geometrical analysis of residuals)
CONCLUSIONS cont.